Disclaimer: This translation is unofficial. Only the original Slovene texts of the laws and regulations have legal effect, and the translations are to be used solely as reference materials to aid in the understanding of Slovene laws and regulations. The Government of the Republic of Slovenia is not responsible for the accuracy, reliability or currency of the translations provided on this web site, or for any consequence resulting from the use of information on this web site. For all purposes of interpreting and applying law to any legal issue or dispute, users should consult the original Slovene texts published in the Official Gazette of the Republic of Slovenia.

Rules on ultralight aircraft (Official Gazette of the Republic of Slovenia [Uradni list RS], No. 49/16)

Pursuant to paragraph two of Article 8, paragraph two of Article 21, paragraph five of Article 31, paragraph eight of Article 32, paragraph two of Article 38, paragraph seven of Article 39, paragraph three of Article 40, paragraphs five and six of Article 43, paragraph three of Article 44 and paragraph six of Article 77 of the Aviation Act (Official Gazette of the Republic of Slovenia [Uradni list RS], No. 81/10 – official consolidated version), the Minister for Infrastructure hereby issues the

RULES

on ultralight aircraft

I. GENERAL PROVISIONS

Article 1

(Subject)

(1) These Rules lay down the term of ultralight aircraft and their division, conditions for their use, maintenance and manufacture, entry in the records of ultralight aircraft, airworthiness of ultralight aircraft, conditions for authorised providers to conduct airworthiness reviews and issue permits to fly, marks and notices of limitations of the ultralight aircraft, minimum equipment of the ultralight aircraft, pilots and other persons, and conditions for training, exams, licences and authorisations of pilots of the ultralight aircraft.

(2) These rules do not apply for powered paragliders without a chassis and powered hang-gliders without a chassis, for which the regulations governing hang-gliders and paragliders apply.

Article 2

(Competent authority)

According to these Rules, the Civil Aviation Agency of the Republic of Slovenia (hereinafter: the Agency) is the competent supervision authority.

Article 3

(Definition and division of ultralight aircraft)

(1) Ultralight aircraft (hereinafter: the aircraft) is an aircraft of a special category, powered or not, that is steered in the air around two or three axes by means of rudder deflection or centre of gravity movement or the combination of both, and for the use of which the homologation of the aircraft type is not required.

(2) The aircraft may be single seaters or two seaters, with or without a pilot, and are divided into the following categories:

- powered ultralight aeroplanes,

- ultralight helicopters,

- ultralight gyroplanes,

- powered paragliders with a chassis,

- powered hang-gliders and powered hang-gliders with a chassis,

- ultralight gliders, and

- unmanned aircraft.

(3) The aircraft referred to in the preceding paragraph also include aircraft for which the type certificate or certificate of airworthiness or permit to fly is not issued on the basis of Regulation (EC) No 216/2008 of the European Parliament and of the Council of 20 February 2008 on common rules in the field of civil aviation and establishing a European Aviation Safety Agency, and repealing Council Directive 91/670/EEC, Regulation (EC) No 1592/2002 and Directive 2004/36/EC (OJ L 79, 19.3.2008, p. 1) and its implementing rules, and which fall into one of the following categories:

- aeroplanes, helicopters and powered parachutes having no more than two seats and a maximum take-off weight (MTOW) of no more than:

- 300 kg for a land plane/helicopter, single-seater; or

- 450 kg for a land plane/helicopter, two-seater; or

- 330 kg for an amphibian or floatplane/helicopter single-seater; or

- 495 kg for an amphibian or floatplane/helicopter two-seater, provided that, where operating both as a floatplane/helicopter and as a land plane/helicopter, it falls below both MTOW limits, as appropriate; or

- 472.5 kg for a land plane, two-seater equipped with an airframe-mounted total recovery parachute system; or

- 315 kg for a land plane single-seater equipped with an airframe-mounted total recovery parachute system and, for aeroplanes, having a stall speed or minimum steady flight speed in the landing configuration not exceeding 35 knots’ calibrated air speed (CAS);

- single and two-seater gyroplanes with a maximum take-off mass not exceeding 560 kg;

- gliders with a maximum empty mass of no more than 80 kg when single-seater or 100 kg when two-seater, including those which are foot launched;

- unmanned aircraft with an operating mass of no more than 150 kg, except those models that do not endanger flight safety;

- any other aircraft which has a maximum empty mass, including fuel, of no more than 70 kg.

(4) As regards the requirements for approval testing, gliders with an auxiliary motor are placed in one of the classes referred to in point 1 of the preceding paragraph.

II. CONDITIONS FOR THE AIRCRAFT USE AND MAINTENANCE

Article 4

(Aircraft use)

The aircraft may be used for flying if:

it is entered in the records or register of aircrafts;

it fulfils the conditions for safe flight and its permit to fly is valid,

its required liability insurance is concluded,

a pilot or person operating the aircraft has the required licence, and

it fulfils other requirements set out by the flight rules.

Article 5

(Purpose)

(1) The aircraft may not be used for sports and recreational flying, for the training of aircraft pilots, aerial work as determined by the ICAO Manual on Aerial Work (ICAO Doc 9408) or marketing. The use of the aircraft for the transport of passengers, goods or mail against payment or compensation is not permitted.

(2) The aircraft may only be used in accordance with the intended use as entered in the permit to fly the aircraft referred to in Article 24 of these Rules.

Article 6

(Airports and aerodromes)

Aircraft take-off and land at airports and aerodromes that are appropriate for an individual aircraft category in accordance with the airport or aerodrome operating manual.

Article 7

(Flight regulations, noise and limitations)

(1) The aircraft may fly in the airspace of the Republic of Slovenia in accordance with the regulations governing aircraft flight rules.

(2) The aircraft may fly within a time period from half an hour before sunrise to half an hour after sunset, when the conditions for visual flight rules (VFR) are fulfilled.

(3) Noise caused by the powered aircraft, when flying 300 metres above the surface of the earth (QFE) with full power and maximum horizontal speed, shall not exceed 65 dB or 78 dB for a gyroplane, measured from the ground, unless a different value is set out by the regulations on the aircraft noise. The noise of the aircraft during a flight, of which at least 51 per cent is built by an amateur, or a non-profit making association of amateurs, for their own purposes and without any commercial objective, may be instrumentally established by comparison with the noise of another aircraft that meets the requirements of this paragraph.

(4) Flying over specific areas, that are declared restricted or conditionally restricted areas pursuant to the law, is prohibited.

(5) The aircraft may fly in uncontrolled Class G airspace as published in the Aeronautical Information Publication (AIP) of the Republic of Slovenia.

(6) The aircraft may fly below the minimum height that is set out for visual flight in accordance with the regulations governing aircraft flights, if the minimum safety height which ensures successful landing in case the engine stops is provided.

(7) Notwithstanding the preceding paragraph, the aircraft must fly a minimum of 300 metres above groups of people and 50 metres above overhead power lines, roads, railways, cableways, antenna systems and other similar facilities, if the height which ensures successful landing in case the engine stops is thereby provided.

Article 8

(Flying of the aircraft in controlled airspace)

(1) Flying of the aircraft in controlled airspace is prohibited, except in cases referred to in paragraphs two, three and five of this Article.

(2) The competent air traffic service may, in exceptional circumstances, permit flying of the aircraft in controlled airspace, if exceptional occurrences during flight, in accordance with the regulations governing aircraft flights, are in place.

(3) Notwithstanding paragraph one and two of this Article, the flying of the aircraft in controlled airspace is permitted in case of the following types of flights:

- at air shows, provided that the aircraft is equipped with an appropriate radio station;

- in the CTR of the airport, where the flying of the aircraft is managed in an approved manner and in accordance with the conditions for safe flight, when the landing speed of the aircraft is at least 38 knots, provided that the aircraft is equipped with an appropriate radio station and transponder, and the pilot holds an authorisation for flying in controlled airspace or a private or sports pilot licence (LAPL or PPL) or higher licence issued in accordance with Commission Regulation (EU) No 1178/2011 of 3 November 2011 laying down the technical requirements and administrative procedures related to civil aviation aircrew pursuant to Regulation (EC) No 216/2008 of the European Parliament and of the Council, OJ L 311, 25.11.2011, p. 1, as last amended by Commission Regulation (EU) 2016/539 of amending Regulation (EU) No 1178/2011 as regards pilot training, testing and periodic checking for performance-based navigation (OJ L 91, 7.4.2016, p. 1, hereinafter: Regulation 1178/2011/EU); if so provided in the approved procedures for safe take-offs and landings at a certain airport, a transponder is not necessary for flying in the airport zone;

- in other parts of controlled airspace if the cruising speed of the aircraft exceeds 76 knots, provided that the aircraft is equipped with an appropriate radio station and transponder, if a transponder is required according to the airspace classification and the pilot shall hold an authorisation for flying in controlled airspace or a private or sports pilot licence (LAPL or PPL) or higher licence issued in accordance with Regulation 1178/2011/EU.

(4) If the conditions referred to in the previous paragraph regarding the travelling speed and equipment with a radio station and transponder are not fulfilled, the air traffic services provider shall reject a flight plan. The air traffic services provider shall also reject a flight plan if the traffic conditions, air traffic flow or obligations in respect of supervision of airspace of the Republic of Slovenia and external borders of the European Union do not enable safe performance of flight of an ultralight or any other aircraft.

(5) Before the performance of a flight in controlled airspace, a flight plan shall be submitted by the aircraft pilot to a competent air navigation services provider. An air navigation services provider shall reject a flight plan and a flight in controlled airspace if the traffic circumstances in the airspace of the intended flight do not provide for the safe performance of that flight.

(6) Notwithstanding the provisions of this Article, the schooling of the aircraft pilots in controlled airspace is permitted if the following conditions are fulfilled:

the aircraft flight instructor holds an authorisation for flying in controlled airspace or at least a private or sports pilot licence (LAPL or PPL) in accordance with Regulation 1178/2011/EU, with an authorisation for the aircraft category,

the aircraft fulfils the conditions regarding the equipment,

a competent air traffic services provider has not rejected a flight plan.

Article 9

(Territorial validity of permit to fly aircraft and international flights)

(1) A permit to fly aircraft issued pursuant to Article 24 of these Rules applies only for flying in the Republic of Slovenia.

(2) For flying in another country, the permission or consent of the competent authorities of the country where the aircraft is headed and of any other country it intends to overfly shall be obtained.

(3) International flight shall be performed to/from an airport or airports open to international air traffic and in accordance with the requirements referred to in the preceding paragraph if the flight shall be performed in controlled airspace. Entry into the airspace of another country shall be performed in accordance with the requirements of the country entered unless otherwise provided by an international treaty or agreement between the competent air navigation services of the countries concerned.

(4) Notwithstanding the provisions of this Article, a flight within the Schengen area may be performed to/from any airport intended for domestic flights, if the conditions referred to in paragraph two of this Article are fulfilled.

Article 10

(Flying of foreign aircraft)

Foreign aircraft may fly in Slovenian airspace on the basis of a flight plan, in which the UL (ultralight) abbreviation is given in the notes, if the following conditions are fulfilled:

- the foreign aircraft has a permit to fly or another relevant document within the meaning of Article 24 of these Rules that has been issued by a competent authority of another country for flying the aircraft in that country;

- foreign aircraft pilots hold a valid pilot’s licence for such a category of aircraft and the airspace where they intend to fly, issued by a competent authority of a foreign country;

- the foreign aircraft holds the compulsory insurance certificate applicable in the territory of the Republic of Slovenia;

- the foreign aircraft meets the conditions regarding noise emissions referred to in paragraph three of Article 7 of these Rules,

- the foreign aircraft has a radio station certificate, if it is carried on board;

- the foreign aircraft and pilot meet the conditions referred to in Articles 31 and 35 of these Rules.

III. AIRCRAFT MANUFACTURE

Article 11

(Categories of manufacture of the aircraft)

The aircraft may be built by amateurs or may be series-produced.

Article 12

(Amateur construction of the aircraft)

An amateur-built aircraft is an aircraft of which at least 51 per cent is built by an amateur, or a non-profit making association of amateurs, for their own purposes and without any commercial objective.

Article 13

(Application of regulations on amateur construction of aircraft)

For the amateur construction of aircrafts, the regulations governing the amateur construction of aircrafts shall apply.

Article 14

(Series production of the aircraft)

(1) Series production of the aircraft means the manufacture of the aircraft, its assemblies, parts and equipment by the authorised manufacturer that is based on the type approval of the aircraft.

(2) Series production of the aircraft without the aircraft approval referred to in Article 15 of these Rules is not permitted.

Article 15

(Type approval of the aircraft)

(1) Type approval of the aircraft is a document by means of which it is certified that a certain type of the aircraft meets the requirements referred to in Articles 16 and 17 of these Rules.

(2) Approval testing is a procedure by means of which it is established whether the type of the aircraft meets the requirements referred to in Articles 16 and 17 of these Rules and the provisions of the flying and maintenance manual, which is established by testing.

(3) The testing referred to in the preceding paragraph may be carried out by persons that have obtained an authorisation issued by the Agency by means of which their fulfilment of the conditions regarding the premises, equipment with technical means for work, personnel and operating and technical procedures for approval testing are proved, as defined in the organisation manual. The testing shall be conducted under the supervision of an authorised official of the Agency.

(4) As regards the fulfilment of the conditions referred to in the preceding paragraph, the regulations referred to in paragraph 3 of Article 19 of these Rules shall apply mutatis mutandis.

(5) After successful approval testing, the type approval of the aircraft shall be issued on the basis of the following:

- technical documentation on the aircraft’s production,

- calculations and reports on the aircraft’s testing,

- aircraft flying and maintenance manual, and

- reports on the concluded testing.

Article 16

(Technical documentation on the aircraft type production)

Technical documentation on the aircraft type production referred to in the preceding Article shall include the following:

- sketch of the aircraft in three projections, components of the main assemblies and especially complicated assemblies and sketches of the details according to which the aircraft can be manufactured,

- list of materials, semi-manufactured products and products from which the aircraft is manufactured,

- aerodynamic calculation of the aircraft calculating its stability and steerability,

- static calculation of the aircraft containing the results of testing of the aircraft’s strength,

- calculation of masses of all parts of the aircraft, payload, fuels and lubricants, mass of the pilot and calculation of the centre of gravity position and the maximum take-off mass of the aircraft,

- description of the technological procedures used in its production.

Article 17

(Calculating and testing of the aircraft type)

(1) Aircraft calculation and testing referred to in Articles 15 and 16 of these Rules shall be determined with the approved technical requirements for the manufacture of an individual category of the aircraft subject to prior approval of the Agency on a proposal by the manufacturer.

(2) Testing of the aircraft type shall be conducted according to a test plan on the ground and in the air, subject to prior approval of the Agency on a proposal by the manufacturer. Testing shall not be shorter than 30 hours of flying, it shall consist of a minimum of 60 take-offs and landings and shall include at least:

lifting to the upper performance limit of the aircraft,

flights which correspond to the biggest autonomy of flight, shortened by 20 minutes,

flights with the highest and lowest speed for certain aeroplane configurations (e.g. position of chassis and flags, etc.),

flights under conditions of the aeroplane’s centre of gravity border positions,

flights with the maximum take-off mass.

(4) Testing of the type of the aircraft in the air may be carried out by the aircraft test pilot. A testing diary is kept by the manufacturer, whereby each test is documented separately.

(5) Once testing on the ground is concluded and the test flights have been carried out, an authorised official of the Agency shall write a report on the aircraft's capability in accordance with the approval requirements for a certain type of the aircraft.

(6) Based on the test report referred to in the preceding paragraph, the manufacturer shall draw up an aircraft type flying and maintenance manual.

Article 18

(Aircraft flying and maintenance manual and the aircraft’s maintenance)

(1) The aircraft flying and maintenance manual shall contain data and instructions on the following:

- purpose,

- mass,

- area of permitted movement of the centre of gravity,

- capabilities,

- stability and steerability,

- restrictions on use,

- maintenance,

- drive and its maintenance (does not apply for ultralight gliders), and

- pre-flight inspection, assembling, disassembling and storage of the aircraft.

(2) The owner is responsible for the maintenance of the aircraft according to the manual, and the aircraft pilot for the pre-flight inspection.

(3) Annual inspections according to the aircraft flying and maintenance manual, published by the manufacturer, are mandatory for the aircraft. The annual inspections shall be carried out by the owner of the aircraft or another person authorised by the owner.

(4) The owner of the aircraft must ensure the keeping of an aircraft logbook, issued by the Agency, on a regular basis. The owner of the aircraft is responsible for the keeping of the aircraft logbook on a regular basis and for the accuracy of the data therein.  The aircraft logbook must be kept by the owner of the aircraft as permanent documentation.

(5) Only those changes and major repairs, for which the technical documentation referred to in Article 16 of these Rules is drawn up and which is approved by the Agency, may be carried out on the aircraft.

Article 19

(Production authorisation)

(1) Before commencement of the production of a certain type of the aircraft, the manufacturer must obtain a production authorisation issued by the Agency for each particular type of the aircraft.

(2) Production authorisation for a certain type of the aircraft shall be issued if the applicant, in addition to the general conditions, prescribed for the pursuit of such an activity, also fulfils special conditions regarding the premises, personnel, operative and technical procedures, equipment and organisation of the quality control system, as defined by the manufacturer’s organisation manual approved by the Agency.

(3) As regards the fulfilment of the conditions referred to in the preceding paragraph, the regulations governing special conditions for the construction and changes of an aircraft, engine, propeller, parachute or the aircraft’s equipment, method of drawing up the technical and technological documentation and technical supervision of the construction shall apply mutatis mutandis.

(4) Along with the production authorisation application for a certain type of the aircraft, the applicant shall enclose the following:

- type approval of the aircraft they wish to produce with the accompanying technical documentation referred to in point 1 of paragraph five of Article 15, and

- data and documentation regarding the fulfilment of the conditions referred to in paragraph two of this Article.

Article 20

(Quality control of the aircraft’s production)

(1) The aircraft manufacturer must ensure quality control of the production that is carried out by the quality inspector in accordance with the manufacturer’s organisation manual. The quality inspector must have appropriate education and necessary experience that correspond to the complexity of the production.

(2) Following its manufacture, each aircraft must be tested on the ground and in the air. Testing that shall be documented must be carried out according to the test plan of the series-produced aircraft, approved by the Agency on the manufacturer’s proposal.

(3) The testing of the aircraft in the air may be carried out by a pilot with a minimum of 200 hours logged of solo flying on the type of aircraft under test who is familiar with the testing techniques, aircraft type, flying manual, test plan and purpose of the test flight. Fulfilment of the conditions shall be documented by the manufacturer. For those pilots who are testing the aircraft in the air, 100 hours of flight time shall be acknowledged if they have a minimum of 100 hours of solo flight time logged as pilots with a licence obtained on the basis of Regulation 1178/2011/EU.

Article 21

(Manufacturer’s certificate of conformity of the aircraft)

(1) Following the successful testing of the aircraft, the manufacturer’s certificate of conformity of the aircraft shall be issued for each aircraft by means of which the manufacturer certifies that the aircraft is capable of safe flying.

(2) The manufacturer’s certificate referred to in the preceding paragraph shall be issued on the ULN-01 form which, as an Annex, forms an integral part of these Rules. .

(3) To the certificate referred to in the preceding paragraph, the manufacturer shall enclose the following:

- flight test report,

- weight and centre of gravity report,

- geometry control report,

- standard and additional equipment list.

Article 22

(Costs of the approval testing procedure for the aircraft)

Costs of the approval testing procedure for the aircraft type shall be borne by the investor.

IV. ENTRY IN RECORDS AND CAPABILITY OF THE AIRCRAFT TO FLY

Article 23

(Entry of the aircraft in records)

(1) In the Records of Aircrafts of the Republic of Slovenia (hereinafter: the Aircraft Records), an aircraft that has Slovenian or foreign approval for a certain type of the aircraft or that has other appropriate document that can be acknowledged pursuant to this Article shall be entered.

(2) The aircraft that was manufactured abroad may be entered in the Aircraft Records upon application of the owner. The application must contain the following:

evidence of the aircraft’s ownership,

aircraft type approval,

aircraft flying and maintenance manual ,

documentation showing according to which technical requirements for manufacture the aircraft was manufactured, and

in case of used aircraft, evidence of the practices of maintenance for the last three years.

(3) Entry of the aircraft referred to in the preceding paragraph in the Aircraft Records shall be rejected if the aircraft does not meet the technical requirements applicable in the Republic of Slovenia or if the ownership of the aircraft and adequacy of the aircraft type approval is not demonstrated for the aircraft type or if the aircraft flying and maintenance manual lacks the necessary content and requirements for its safe use and flying or if it is evident from the submitted evidence of the practices of maintenance that the used aircraft has not been maintained.

(4) If certain technical requirements for the manufacture of an aircraft or aircraft equipment, for which the applicant request the entry in the Aircraft Records, have not been set out yet in the Republic of Slovenia, the applicant shall also attach the technical requirements for the aircraft manufacture and the list of the aircraft equipment to the application for entry of the aircraft in the Aircraft Records.

(5) Type approval of aircraft or other appropriate document for a certain type of aircraft, issued by another country or authority of this country, shall be acknowledged on the basis of appropriate technical documentation and tests in the air if the aircraft meets at least the requirements of the Slovenian regulations or requirements of the foreign regulations that are equivalent to the Slovenian ones.

(6) In case the ownership of the aircraft is changed, the inspection of the aircraft and the update of data by recording the transfer of ownership in the aircraft logbook, made by the owner of the aircraft or a person authorised by the owner of the aircraft, are mandatory. The previous owner must declare in written form to the new owner that the inspection has been made and the data in the aircraft logbook are correct.

(7) Entry of the amateur built aircraft in the Aircraft Records is not permitted.

Article 24

(Aircraft airworthiness and permit to fly the aircraft)

(1) Aircraft airworthiness means capability of the aircraft to fly, which is established by the Agency or another authorised provider.

(2) At the request of owner or user of the aircraft, the Agency shall issue a permit to fly aircraft, for which the fulfilment of the conditions for safe flight pursuant to Articles 24, 25 and 26 of these Rules is established.

(3) To the application for permit referred to in the preceding paragraph, the applicant shall enclose the following:

- report from the commission, drawn up in accordance with the regulations governing the amateur built of aircrafts, or type approval of the aircraft in case the aircrafts are series-produced,

- aircraft flying and maintenance manual,

- certificate showing that the noise of the aircraft does not exceed the limitations set out in these Rules (does not apply for the aircrafts without engine),

- a radio station certificate, if it is carried on board, and

- the manufacturer’s certificate of conformity of the aircraft.

(4) Permit to fly aircraft is a certificate of capability of the aircraft to fly safely and evidence of its entry in the Aircraft Records.

(5) Permit to fly aircraft shall be issued on the ULN-02 form which, as Annex, forms an integral part of these Rules.

(6) Permit to fly aircraft must be placed in or on aircraft during a flight or carried by the aircraft pilot.

(7) Certificate referred to in point 3 of paragraph three of this Article shall be issued by a person that has an authorisation to conduct the noise measurements.

Article 25

(Establishment of the airworthiness of aircraft)

(1) The airworthiness of the aircraft shall be established by means of the following:

- review of the aircraft and its documentation,

- test of the aircraft on the ground, and

- test of the aircraft in the air.

(2) With the review of the aircraft, it shall be established whether the aircraft corresponds to the aircraft type approval. With the review of the documentation of the aircraft, it shall be established whether the flying and maintaining of the aircraft was carried out in accordance with the aircraft flying and maintenance manual. Review also includes the control of implementation of the airworthiness and technical requirements.

(3) With the test on the ground, the operation of all systems of the aircraft and of the engine in all of its operating fields shall be established. Operating of the aircraft’s systems shall be established according to the aircraft flying and maintenance manual, and the operating of the engine according to the engine’s manufacturer plan.

(4) Test of the aircraft in the air means a test of the aircraft within the limitations set out in the aircraft flying and maintenance manual. Test of the aircraft in the air shall be carrying out by the aircraft pilot who has minimum 100 hours of solo flying logged on the appropriate aircraft category.

(5) In order to establish the airworthiness of the aircraft, the provisions of regulations governing the procedure and method of establishment of the airworthiness of aircrafts shall apply mutatis mutandis if they do not contravene the provisions of these Rules.

Article 26

(Validity of permit to fly aircraft)

Permit to fly aircraft is valid for a period of one year and may be extended in accordance with the preceding Article.

Article 27

(Authorised provider)

(1) In order to obtain the authorisation to conduct the airworthiness reviews, the authorised provider must have appropriate premises, technical equipment and organisation manual that shall be approved by the Agency before it is issued.

(2) Organisation manual referred to in the preceding paragraph must:

- demonstrate the professional qualifications of the personnel pursuant to Article 28 of these Rules and the method of maintaining their qualifications, have a system of authorising such personnel established and procedures for determination of competences developed, and prove the appropriate leadership and control of these procedures within its organisational structure. Procedures approved by the Agency must clearly specify limits within which the authorisations are issued to personnel;

- have established control system of continuing airworthiness, meaning that the authorised provider must:

- prove that it has a system of control of the continuing airworthiness established, which is maintained in such a way that the periodic reviews of airworthiness can be carried out and the permits to fly aircrafts, for which it is authorised, extended;

- ensure that the continuing airworthiness of each aircraft, for which it conducts the airworthiness review, shall be such that:

- the aircraft remains within the approved configuration,

- all aircraft changes are approved,

- all requirements and recommendations of the aircraft’s manufacturer are meet,

- entire regulatory maintenance is carried out,

- instruments were reviewed, tested and approved in accordance with the requirements,

- checking of the aircraft during a flight was conducted according to the approved programme of checking in the air,

- mass and position of the centre of gravity satisfy the requirements;

- have process of carrying out the airworthiness review established for every aircraft, the airworthiness of which it supervises, which satisfies the requirements of these Rules;

- indicate the following information:

- statement of the accountable manager confirming that the manual and the related documents comply with these Rules;

- general description of the scope of works according to the authorisation;

- titles, names and functions of the following persons that are regarded as mandatory:

- responsible manager;

- technical manager of supervision of the continuing airworthiness of aircrafts;

- quality control assurance manager;

- organisation chart presenting the lines of duties;

- list of persons authorised to carry out the airworthiness reviews of aircrafts and issuing or extending the permit to fly;

- general description of the personnel needs of the authorised provider considering the scope of works;

- procedures that describe how the authorised provider ensures compliance with these Rules;

- the procedure of notifying the Agency about organisational and other changes of the authorised provider;

- procedure for approval of changes to the organisation manual of the authorised provider;

- record of or reference to any aircraft, the airworthiness review of which is conducted by the authorised provider;

- detailed description of the system and principles of record keeping;

- general description of premises at each address of the authorised provider, given in the authorisation;

- procedure of supplementing or changing the organisation manual as necessary in order to maintain its content in accordance with the situation of its organisation;

- have the system of quality control established, which:

- once the authorisation is granted, furnishes the Agency with the supervision in the entire organisation of the authorised provider led by the accountable manager, as defined in organisation manual, and provides supervision over the standards and requirements as well as their amendments, as evident from the authorisation,

- proves that it has a documented system of quality control established and maintained,

- provides compliance with the requirements of these Rules and has the quality control system manager who monitors the adequacy and regularity of the procedures necessary to ensure the airworthiness of aircrafts, while the monitoring of adequacy must include the feedback to the accountable manager for implementation of necessary corrective measures,

- determines that, for meeting the requirements referred to in the preceding point, the authorised contractor shall establish the internal audit programme, acceptance for the Agency;

- determines that the Agency has, at all reasonable times, access to all data, reports and records directly or indirectly linked with the checking of aircrafts during a flight, airworthiness of aircrafts, engines, propellers and parts of the aircrafts, and that it has the right to be present at functional checking or testing linked in any way with the establishment of airworthiness or capability of the aircrafts, engines, propellers of the components of the aircrafts to fly

(3) The authorised provider must take out liability insurance.

(4) The first permit to fly shall be issued by the authorised provider, followed by the airworthiness review and extension of the permit to fly by the personnel of the authorised provider.

(5) The authorised provider is entitled to charge a fee for the services referred to in this Article in accordance with the applicable tariff for the provision of services of the Civil Aviation Agency of the Republic of Slovenia.

(6) The authorised contractor is obliged to notify the Agency about issuing or extending the permit to fly no later than within ten days.

Article 28

(Personnel of the authorised contractor)

(1) Personnel of the authorised contractor that carries out the airworthiness reviews and issues the permits to fly, must fulfil the following conditions:

minimum age of 21 years,

passing of the professional exam on administrative procedure,

evidence of introductionary training for at least one type of the aircraft, obtained by the manufacturers of the aircraft types or organisations, authorised by the manufacturers of the aircraft types,

any licence in accordance with Part-66 of Appendix III to Commission Regulation (EU) No 1321/2014 of 26 November 2014 on the continuing airworthiness of aircraft and aeronautical products, parts and appliances, and on the approval of organisations and personnel involved in these tasks (OJ L 362, 17.12.2014, p. 1), as last amended by Commission Regulation (EU) 2015/1536 of 16 September 2015 amending Regulation (EU) No 1321/2014 as regards alignment of rules for continuing airworthiness with Regulation (EC) No 216/2008, critical maintenance tasks and aircraft continuing airworthiness monitoring (OJ L 241, 17.9.2015, p. 16; hereinafter: Regulation 1321/2014/EU), or

minimum secondary education with evidence of passing modules M7a, M9a, M10, M12, M16 and M17a for a category A licence, module M11b for ultralight aeroplanes and module M12 for ultralight helicopters and gyroplanes in accordance with Part-66 of Regulation 1321/2014/EU), and five years of work experience in the aircraft maintenance, or

valid licence for the aircraft pilot for at least 5 years and completed basic training course for maintenance of at least one type of the aircraft’s engine, or

minimum five years of work experience as the quality inspector for aircrafts in the production organisation for the aircraft construction or as quality controller of the amateur built aircrafts.

(2) Authorised contractor is obliged to ensure that its personnel maintains competences, whereby two airworthiness reviews carried out per year or completed training which refers to the airworthiness extension are considered as maintenance of competences.

Article 29

(Supervision over the authorised contractor)

(1) Supervision of the work of authorised contractor shall be exercised by the Agency.

(2) If the evidence exist that the authorised contractor does not meet the requirements referred to in Articles 27 and 28 of these Rules, the findings defined according to the following levels shall be made:

a level one finding is any non-compliance with the requirements that lowers the safety standard and jeopardizes the air safety,

a level two finding is any non-compliance with the requirements that does not graduate as the level one finding.

(3) After receiving the notification of findings:

the authorised provider proposes a plan of corrective measure that identifies possible systemic cause and contains the analysis in order to prevent recurrence. The corrective measures shall be submitted to the Agency for approval within agreed time interval;

for the level one finding, the Agency may propose to the minister responsible for infrastructure to revoke, limit or entirely or partially suspend the authorisation until the successful implementation of corrective measures;

for the level two finding, the Agency may specify a period for implementation of the corrective measures appropriate to the nature of finding which, at beginning, shall not exceed three months, while in cases, when considering the nature of finding and submission of relevant plan of corrective measures, the deadline for implementation of corrective measures may be extended by the Agency;

in case of unsuccessfully implemented corrective measures in terms of time, the finding shall be raised to the level one finding, while the Agency shall propose to the minister responsible for infrastructure to adopt the measures referred to in indent two of this paragraph.

(4) The authorised provider is obliged to notify the Agency in advance of any change of the following:

firm of the authorised provider,

registered office or location of the authorised provider,

additional locations of the authorised provider,

accountable manager,

any person required by the organisation manual,

premises, procedures, scope of work and personnel if these changes could influence the authorisation of the authorised provider.

Article 30

(Prior checks)

The authorised provider shall obtain authorisation if it fulfils the conditions referred to in Articles 27 and 28 of these Rules, based on the procedure for the assessment of fulfilment of the abovementioned conditions, previously implemented by the Agency.

V. MARKS OF THE AIRCRAFT AND NOTICES OF AIRCRAFT LIMITATIONS

Article 31

(Aircraft registration mark)

Each aircraft must have a registration mark specified in accordance with the regulations governing the registration and other marks of aircrafts.

Article 32

(Identification plate and aircraft serial number)

(1) Each aircraft must have a firmly fixed identification plate with a size of 10 × 5 centimetres and content as specified in form ULN-03 which, as an Annex, forms an integral part of these Rules.

(2) Aircraft must have a firmly fixed serial number on their fuselage and wing, while powered aircraft must also have an engine serial number on their engine and a propeller serial number of their propeller.

Article 33

(Notice of aircraft use)

Each aircraft must, in a visible area of the pilot's or passenger's seat, be equipped with a legible notice that is written in capital letters with a minimum size of 8 millimetres in the Slovene and English languages, indicating that the aircraft does not meet the requirements and standards of recommended practices of the International Civil Aviation Organisation to be issued with a certificate of airworthiness: The notice shall read as follows:

OBVESTILO: ZA TA ZRAKOPLOV NI IZDANO SPRIČEVALO O PLOVNOSTI ZRAKOPLOVA V SKLADU Z MEDNARODNIMI STANDARDI IN PRIPOROČENIMI PRAKSAMI MEDNARODNE ORGANIZACIJE CIVILNEGA LETALSTVA. Z NJIM LETITE NA LASTNO ODGOVORNOST!

NOTICE: THIS AIRCRAFT IS OPERATING WITHOUT A CERTIFICATE OF AIRWORTHINESS ISSUED ACCORDING TO INTERNATIONAL CIVIL AVIATION ORGANIZATION STANDARDS AND RECOMMENDED PRACTICES. FLY AT YOUR OWN RISK.

VI. MINIMUM EQUIPMENT FOR THE AIRCRAFT, AIRCRAFT PILOT AND ANY OTHER PERSON

Article 34

(Equipment of the ircraft)

(1) Powered aircraft must have:

- seat belts deepening on the aircraft category,

- speedometer,

- altimeter,

- fuel meter or possibility of optically controlling the amount of fuel,

- compass,

- recovery system or recovery parachute system or total recovery parachute system (hereinafter: recovery system), if intended by the aircraft’s manufacturer for this aircraft type.

(2) An ultralight glider must have equipment referred to in points 1, 2 and 3 of the preceding paragraph.

(3) Unfastening of seat belts should be possible with one intentional movement.

(4) Powered aircraft used in controlled airspace must also have an appropriate radio station and transponder and other required equipment and devices that are required for a specific airspace.

(5) Aircraft, with the exception of gyroplanes, by means of which aircraft pilot training is provided, must also have a recovery system.

Article 35

(Equipment of the aircraft pilot and of any other person)

(1) On board of an open cabin aircraft, the use of a protective helmet and protective goggles if the helmet does not have a visor is mandatory. To fly the aircraft above lakes and the sea, the use of a life jacket is mandatory in accordance with the flight regulations. On the aircraft, the use of a recovery parachute is mandatory if required by the aircraft flying and maintenance manual.

(2) Aircraft pilots may not allow any person without the requisite equipment to fly simultaneously with them on the same aircraft.

(3) During flying in the framework of testing a new aircraft type, with the exception of gyroplanes, test pilots must have an emergency parachute if the aircraft is not equipped with a recovery system.

VII. TRAINING, EXAMS, LICENCES AND AUTHORISATIONS OF AIRCRAFT PILOTS

Article 36

(Conditions for training)

(1) Persons under training to become an aircraft pilot shall meet the following requirements:

- they shall not be younger than 16 years of age;

- regarding medical conditions, they shall either meet conditions set out in the regulations on health requirements that must be fulfilled by a category B motor vehicle driver, which shall be demonstrated by presenting a medical certificate of a completed medical examination of the driver candidate or of the driver, which shall not be older than three months or hold a valid medical certificate for LAPL or higher licence issued in accordance with Regulation 1178/2011/EU;

- before entering practical training, they must have successfully completed the basic theoretical training according to an approved pilot training programme for a specific aircraft category, which shall be demonstrated by a passed written exam;

- they shall be entered in the registry of students with a flight school organisation or another registered flight school they train at;

- if they are younger than 18 years of age, their training application shall be accompanied by their parents’ or guardian's consent;

(2) Aircraft pilot training shall only be conducted according to the training programme for a specific aircraft category approved by the ministry. Requirements applying to training programmes for private or sports pilot licences shall apply mutatis mutandis to these training programmes, unless otherwise provided for by these Rules.

(3) Aircraft pilot training may be conducted by a flight school organisation or another registered flight school that meet the requirements laid down in the regulations on flight crew licensing – aeroplane pilots, unless otherwise provided by these Rules.

(4) Practical training to become an aircraft pilot may be conducted at aerodromes with a runway of a prescribed length and at airports.

Article 37

(Registering for the exam)

(1) For anyone who wants to take the theoretical exam for an aircraft pilot, their application for the exam shall be accompanied by a statement from a registered flight school evidencing that the candidate has completed a specific theoretical training programme.

(2) After the candidate has passed the theoretical exam, they shall take the practical exam within 24 months; otherwise, they shall retake the theoretical exam.

(3) For anyone who wants to take a practical exam for an aircraft pilot, the following must be enclosed along with their registration application:

evidence of the aircraft category flight time as prescribed by the training programme, and

a statement from the aircraft flight instructor indicating that the candidate is qualified to take the exam.

(4) The practical exam for an aircraft pilot may be taken by a person who has attained the age of 17 years.

Article 38

(Aircraft pilot exam and licence)

(1) The exam shall be taken in front of an exam committee that includes at least one member from the list of flight experts. The exam to obtain an aircraft pilot’s licence is comprised of a theoretical and practical part, in line with the training programme for a specific aircraft category. The exam committee shall be appointed by the Agency.

(2) The theoretical part shall comprise the following:

- basics of aerodynamics and flight mechanics (flight theory),

- aviation meteorology,

- structures and materials,

- propulsion group (engine),

- air navigation,

- emergency procedures,

- broadcasting and VFR phraseology,

- aircraft instruments,

- aviation regulations,

- using the aircraft,

- using runways, and

- aviation medicine.

(3) After the candidate has passed the theoretical part of the exam, they shall take the practical part of the exam. The exam flight shall be conducted according to the aircraft pilot training programme set out for each aircraft category in accordance with paragraph two of Article 36 of these Rules.

(4) Based on comparable contents and difficulty, an aircraft pilot holding a licence for a specific aircraft category who wants to obtain an aircraft pilot’s licence for another aircraft category shall be exempt, fully or in part, from taking the theoretical and practical parts of the exam referred to in paragraph two of this Article in accordance with the training programme for another aircraft category.

(5) Based on comparable contents and difficulty, an aircraft pilot candidate who holds a valid sailplane pilot’s licence, private or sports pilot’s licence (LAPL or PPL), commercial pilot’s licence (CPL) or airline transport pilot’s licence (ATPL) shall be exempt, fully or in part, from taking the theoretical part of the exam referred to in paragraph two of this Article. For the practical part of the training, such a pilot shall have logged at least five hours of retraining specified for each aircraft category in accordance with paragraph two of Article 36 of these Rules, except sailplane pilot’s licence holders.

(6) After the exam has been passed, the Agency shall issue an aircraft pilot’s licence.

Article 39

(Aircraft pilot)

(1) The aircraft may be used by persons who hold a valid aircraft pilot’s licence for such an aircraft category, meet the prescribed health requirements and have the aircraft type they are allowed to use entered in the pilot’s logbook.

(2) Under the surveillance of a flight instructor, an aircraft may also be used by a person under training to obtain an aircraft pilot’s licence pursuant to Article 36 of these Rules.

(3) The flight instructor shall check the ability of the aircraft’s pilot to use the aircraft type within a certain aircraft category, that the candidate does not yet have it entered in the pilot’s logbook, during a flight, and shall enter the established ability in the pilot’s logbook.

Article 40

(Aircraft flight instructor)

(1) In accordance with paragraph three of Article 36 of these Rules, training and checking the technical competence of students for aircraft pilots may be performed by an aircraft flight instructor who:

- has logged at least 200 flight hours, of which at least 10 hours are of methodological flying on the aircraft category for which they teach, of which at least three hours are of methodological flying on the aircraft type for which they teach, and have obtained a valid aircraft pilot’s licence at least two years before registering for the exam to obtain a special authorisation for the aircraft flight instructor for a specific aircraft category,

- have passed the exam for a flight instructor for a specific aircraft category, and

- have corresponding authorisation entered in their valid aircraft pilot’s licence.

(2) For anyone who wants to take the exam to obtain authorisation for a flight instructor for a specific aircraft category, the following shall be enclosed along with their application for taking the exam:

- evidence showing compliance with the conditions referred to in point 1 of the preceding paragraph,

- a statement from an aircraft flight instructor indicating that the candidate is qualified to take the exam,

- evidence showing that an aircraft for conducting the exam has been guaranteed.

(3) The aircraft flight instructor may perform training and checking of the technical competence of candidate only on the aircraft type entered in the instructor pilot’s logbook.

(4) Based on comparable contents and difficulty, an aircraft flight instructor candidate with a valid rating for a flight instructor issued in accordance with the regulations on flight crew licensing shall be deemed, fully or in part, as meeting the conditions referred to in points 1 and 2 of paragraph one of this Article, provided they log at least five hours of retraining, which is specified for each aircraft category separately in accordance with paragraph two of Article 36 of these Rules.

(5) The candidates for obtaining aircraft flight instructor authorisation shall be deemed to have logged 100 hours of the requested flight time referred to in point 1 of paragraph one of this Article if they have logged at least 100 hours of autonomous flight hours as pilots with a licence obtained on the basis of Regulation 1178/2011/EU.

Article 41

(Aircraft flight instructor exam)

(1) The flight instructor exam for a specific aircraft category shall be taken in front of an exam committee that includes at least one member from the list of flight experts. The exam is comprised of a theoretical and practical part, in line with the training programme for a specific aircraft category.

(2) The theoretical part shall comprise the following:

- basics of aerodynamics and flight mechanics (flight theory),

- aviation meteorology,

- propulsion group (engine),

- air navigation,

- maintenance,

- emergency procedures,

- broadcasting and VFR phraseology,

- aviation regulations,

- aviation medicine with psychophysiology, and

- teaching methods.

(3) The practical part of the exam comprises an exam flight conducted according to the aircraft flight instructor training programme specified for each aircraft category separately.

(4) The exam for an aircraft flight instructor may be taken by a person who has attained the age of 19 years.

Article 42

(Aircraft test pilot)

(1) Testing of new aircraft categories and types referred to in Article 17 of these Rules may be performed by an aircraft test pilot who meets the following conditions:

- is at least 21 years old,

- has logged at least 200 flight hours, of which at least 100 hours are of methodological flying on the same aircraft category as the one being tested, and has held a valid aircraft pilot’s licence for at least five years,

- has passed the aircraft test pilot exam,

- have corresponding authorisation entered in their valid aircraft pilot’s licence.

(2) For candidates who want to take the exam to obtain authorisation for an aircraft test pilot, the following shall be enclosed along with their application for taking the exam:

- evidence of the aircraft category flight time as prescribed by the training programme,

- a statement from a flight school organisation or another registered flight school indicating they have completed a particular training programme,

- a statement from an aircraft flight instructor indicating that the candidate is qualified to take the exam,

- evidence showing that an aircraft for conducting the exam has been guaranteed.

Article 43

(Aircraft test pilot exam)

(1) The aircraft test pilot exam is comprised of a theoretical and practical part, in line with the training programme for a specific aircraft category.

(2) The theoretical part shall comprise the following:

- aerodynamics and flight mechanics (flight theory),

- aircraft materials and structure,

- testing measurements, methods and procedures, and

- emergency procedures.

(3)The practical part of the exam comprises a series of exam flights conducted according to the approved training programme for an aircraft test pilot, which shall contain all of the elements for aircraft testing before issuing the aircraft type approval.

Article 44

(Authorisation to fly in controlled airspace)

(1) Holders of an aircraft pilot’s licence shall, on their own request, be issued with an authorisation to fly in controlled airspace if they have passed the theoretical and practical parts of the exam to fly in controlled airspace.

(2) The theoretical part of the exam for an aircraft pilot in controlled airspace shall comprise the following:

- air navigation with the basics of radio navigation,

- flight regulations in controlled airspace,

- emergency procedures in controlled airspace, and

- English or Slovene air phraseology.

(3) The practical part of the aircraft pilot exam for obtaining authorisation to fly in controlled airspace covers the exam flights performed according to the approved aircraft pilot training programme for obtaining authorisation to fly the aircraft in controlled airspace which shall include at least:

- two take-offs and two landings in the airport at which the air navigation services operate,

- one circumstance that requires the use of an emergency procedure, and

- two entries into and exits from controlled airspace.

(4) Notwithstanding paragraph one of this Article, holders of valid licences for a private or sports pilot, commercial pilot or airline transport pilot fulfil the requirements to fly the aircraft in controlled airspace if qualified to fly the aircraft type.

Article 45

(Authorisation to pull gliders and banners)

(1) Holders of an aircraft pilot’s licence shall, on their own request, be issued with authorisation to pull gliders and banners if they have logged 50 hours of solo flight time after obtaining the aircraft pilot’s licence and have successfully completed the theoretical and practical parts of the training.

(2) The theoretical and practical parts of the aircraft pilot training shall be performed according to the approved training programme in the registered flight school.

(3) Authorisation to pull gliders or banners shall be entered in the aircraft pilot’s licence on the request of their holders, based on their concluded theoretical and practical training and valid authorisation to pull gliders and banners that is entered in the licence obtained on the basis of Regulation 1178/2011/EU.

Article 46

(Authorisations for aerial work)

(1) In order to conduct aerial work, the operations manual shall be enclosed by the applicant for special authorisation, which must include:

- general description of the scope of aerial work;

- responsible persons;

- operations personnel and training:

- conditions for training providers,

- operations personnel entry requirements,

- initial and periodic training of operations personnel;

- standard procedures in the conduct of aerial work based on a risk analysis;

- aircraft equipment;

- reporting, standard forms.

(2) Aircraft pilots shall carry out the aerial work when they have:

- logged a minimum of 200 hours of flying on a certain aircraft category, including the flight time obtained with other licences,

- a minimum of 10 hours of flying logged on the aircraft category,

- completed medical examination for a category B motor vehicle driver in accordance with regulations on health requirements that must be fulfilled by a category B motor vehicle driver, which shall be demonstrated by presenting a medical certificate of a completed medical examination of the driver candidate or of the driver, which shall not be older than three months, or a valid medical certificate issued in accordance with Regulation 1178/2011/EU when the aerial works are not conducted against payment or a Class II medical certificate in accordance with Regulation 1178/2011/EU when the aerial works are conducted against payment, and

- provided training as defined in the operations manual that shall include:

- knowledge of performance and limitations of a certain aircraft category,

- works in the air and their characteristics,

- knowledge of risks posed by specific aerial work,

- necessary equipment for works in the air,

- aviation meteorology in the area where the aerial works are conducted when it is specific, and

- minimum of four demonstration flights for individual types of aerial works.

Article 47

(Issuing and extending the validity of the aircraft pilot’s licences)

(1) At the request of a person that has passed the aircraft pilot exam or the aircraft flight instructor exam, the Agency shall issue an aircraft pilot’s licence or enter special authorisation of the aircraft flight instructor into the aircraft pilot’s licence. Regarding the taking of exams, the procedure and method of issuing the aircraft pilot’s licence and entering the authorisations and regulations on flight crew licensing – aeroplane pilots shall apply mutatis mutandis unless otherwise provided by these Rules.

(2) A permit to fly the aircraft shall be issued on the ULN-04 form which, as an Annex, forms an integral part of these Rules.

(3) An aircraft pilot’s licence is valid for four years and shall be extended upon the pilot’s application and if the following conditions are fulfilled:

- in case of periodical extensions:

- completed medical examination for a category B motor vehicle driver in accordance with regulations on health requirements that must be fulfilled by a category B motor vehicle driver, which shall be demonstrated by presenting a medical certificate of a completed medical examination of the driver candidate or of the driver, which shall not be older than three months, or a valid medical certificate issued in accordance with Regulation 1178/2011/EU,

- at least 10 hours of flight time logged in the validity period of the licence and a completed control flight with the aircraft flight instructor from the list of instructors in registered flight schools of a minimum duration of 45 minutes or

- in case a candidate does not meet the condition of the required flight time referred to in the preceding indent, a proficiency test shall be taken in front of a committee of a minimum duration of 45 minutes;

- in case of licence extension after its expiry (licence renewal):

- completed medical examination for a category B motor vehicle driver in accordance with regulations on health requirements that must be fulfilled by a category B motor vehicle driver, which shall be demonstrated by presenting a medical certificate of a completed medical examination of the driver candidate or of the driver, which shall not be older than three months, or a valid medical certificate referred to in Article 36 of these Rules.,

- entry in the register of students of the registered flight school with at least 5 hours of flight time performed there,

- proficiency test in front of a committee of a minimum duration of 45 minutes.

(4) The proficiency test referred to in indent three of point 2 of the preceding paragraph shall encompass knowledge of using the aircraft, knowledge of aviation regulations and emergency procedures and checking during a flight.

Article 48

(Pilot logbook)

The aircraft pilot and the candidate for the aircraft pilot shall enter their flying on a certain aircraft category in the pilot’s logbook issued by the Agency. The flight time of the candidate for the aircraft pilot must be confirmed by the aircraft flight instructor.

Article 49

(Participation in air shows)

Aircraft pilots who have a valid aircraft pilot’s licence may participate in air shows and competitions if their total solo flight time with the category of aircraft, with which they participate in the air show or competition, exceeds 100 hours.

VIII. TRANSITIONAL AND FINAL PROVISIONS

Article 50

(Transitional provisions)

(1) Procedures to extend or renew the licence referred to in Article 47 of these Rules, initiated prior to the entry into force of these Rules, shall be concluded according to the regulations applicable to date.

(2) Holders of the aircraft pilot’s licence shall obtain the medical certificate referred to in point 2 of paragraph one of Article 36 of these Rules upon the aircraft pilot’s licence extension.

Article 51

(End of validity)

On the day these Rules enter into force, the Rules on ultralight aircraft (Official Gazette of the Republic of Slovenia [Uradni list RS], No. 107/08) shall cease to be in force.

Article 52

(Date of application)

Notwithstanding Article 53 of these Rules, the Slovene phraseology referred to in point 4 of paragraph 2 of Article 44 of these Rules shall apply as of 1 January 2017.

Article 53

(Entry into force)

These Rules shall enter into force on the day after its publication in the Official Gazette of the Republic of Slovenia.

No. 007-276/2015/65-0191422

Ljubljana, 5 July 2016

EVA 2015-2430-0063

Peter Gašperšič, PhD

Minister
for Infrastructure

Annex: Forms